DIGITAL AUDIO SERVER

QUICKSTART INSTALLATION INSTRUCTIONS

Your receiver is programmed for Big D & Bubba on audio & cue relay port 1.  Once installed, please contact network support for activation.

INTRODUCTION

This Quick Start guide instructs you on how to quickly set up and start operating your i6420 Professional media server in order to receive WestwoodOne programming. For additional information please go to

www.dg-tech.net

This receiver is a replacement using the same satellite, LNB and dish as your existing receiver. Please expedite the installation of this receiver as it must be installed and online no later the four weeks from the original ship date on your packing list from the manufacturer.

Contact Network Services between 8AM and 10PM Eastern Monday through Friday at (888) 435-7450 for:

- Installation Questions

- Authorization of the receiver after installation.

Version 1.00.00 11/15/11

Safety Summary

The iPump 6420 is designed for safe use with few special precautions required of the user. The following items are basic precautions to use when installing and working with your iPump 6420:

Do not open the iPump 6420's chassis cover.

Location and Mounting

The iPump 6420 should be mounted in a standard 19-inch equipment rack. After mounting, maintain a clean, dry environment for the unit.

Precautions

WARNING

This is a Class A product. In a domestic environment this product may cause radio interference for which the user may need to take mitigating action.

DANGER

To avoid damage to this and other equipment, or personal injury, the following items should be strictly observed.

Elevated Operating Ambient

When equipment is installed in a closed or multi-unit rack assembly, the operating ambient temperature of the rack environment may be greater than the room ambient temperature. Therefore, consideration should be given to the ambient air temperature within the rack, and not just inside the room, when deciding if the maximum recommended ambient operating temperature (TMRA) is being met.

Reduced Air Flow

Equipment should be installed such that airflow required for safe operation of the equipment is not compromised. Units may be stacked with other rack-mount equipment without gaps. However, to ensure adequate air flow, leave rear and front vents unobstructed. Providing1/2 inch clearance for the right side air vents results in a longer product life for the iPump 6420.

Mechanical Loading

Mounting of the equipment in a rack should be such that a hazardous condition is not produced by uneven loading. This unit is not very heavy, but total rack loading must be considered. Also, do not rest any unsupported equipment on your iPump 6420.

DANGER

Circuit Overloading

Consideration should be given to the connection of the equipment to the supply circuit and the effect that overloading of circuits could have on over-current protection and supply wiring. Ensure that the total rack or breaker power consumption does not exceed the limits of the ac branch circuit. Appropriate consideration of equipment ratings should be used when addressing this concern.

Reliable Earthing

Reliable earthing of rack-mounted equipment should be maintained. Particular attention should be given to supply connections other than direct connections to the branch circuit (use of power strips, chassis ground lugs, etc.).

Lithium Battery

Proper disposal and replacement of the motherboard’s lithium battery is necessary. Replacing the battery with an incorrect type presents the risk of explosion. Dispose of used batteries according to the package instructions.

Telecommunication Line Cord

To reduce the risk of fire, use only No. 26 AWG or larger telecommunication line cord.

Rack Installation Procedure

The iPump 6420 is sized at 1 RU and will fit an EIA-standard, 19-inch-wide equipment rack.

1) Install angle brackets or cross-supports capable of supporting both the unit and its connecting cables. Screw or bolt the supports securely to the equipment rack.

2) Place the iPump 6420 on its supports and use four anchor screws or bolts and nuts to secure the unit's front brackets to the rack.

WARNING

Do not block any of the ventilation or fan opening on the front, side, or rear of the unit. Support arrangements that do not allow adequate air flow or that block the openings on front, side and rear vents may result in overheating and damage to the iPump 6420.

WARNING

The front brackets must be secured to the rack. If front brackets are left unsecured, the unit may shift forward and fall from the rack during installation or operation. Failure to secure the front brackets may result in personal injury and/or damage to the equipment.

WARNING

Locate the iPump 6420 and its cables to avoid impacts, spills, and pulling cables and to ensure sufficient air flow. Failure to locate the iPump 6420 in a proper environment may result in damage to the equipment.

# Text boxes

888-435-7450